TRACK 3 — RHCSA ADMINISTRATION
LVM — Create, Extend, Reduce Safely
Logical Volume Management (LVM) adds a flexible abstraction layer between physical storage and filesystems. It lets you resize, snapshot, and reorganise storage without downtime. Resource: Notes
03-rhcsa/lvm.md

---
Objectives — What You Will Learn
▶ LVM concepts
▶ Create an LVM setup from scratch
▶ Extend an LV (online, no downtime)
▶ Reduce an LV (ext4 only — not XFS)
▶ Add a new PV to an existing VG
▶ LVM snapshot (basics)
▶ LVM status commands

---
LVM concepts
• Term: Description
• PV (Physical Volume): A disk or partition initialised for LVM
• VG (Volume Group): A pool of storage from one or more PVs
• LV (Logical Volume): A slice of a VG; behaves like a partition
• PE (Physical Extent): Smallest allocation unit (default 4 MiB)
Physical disk(s) └── Physical Volume (PV) [pvcreate] └── Volume Group (VG) [vgcreate] ├── Logical Volume (LV) [lvcreate] └── Logical Volume (LV) └── Filesystem (mkfs.xfs) └── Mount point

---
Create an LVM setup from scratch
• Assumes a raw extra disk /dev/vdb (adjust to your device).

---
Extend an LV (online, no downtime)
• Or extend and grow in one command:
• (-r = resize filesystem automatically after extending)
# Extend LV by 2 GB sudo lvextend -L +2G /dev/datavg/datalv # Grow XFS filesystem to fill (online) sudo xfs_growfs /mnt/data

---
Extend an LV (online, no downtime) (cont.)
sudo lvextend -L +2G -r /dev/datavg/datalv

---
Reduce an LV (ext4 only — not XFS)
• ⚠️ XFS cannot be shrunk
• Reduction only works with ext4. For XFS, create a new LV at the right size.
# ext4 only — unmount first sudo umount /mnt/data sudo e2fsck -f /dev/datavg/datalv sudo resize2fs /dev/datavg/datalv 4G sudo lvreduce -L 4G /dev/datavg/datalv sudo mount /dev/datavg/datalv /mnt/data

---
Add a new PV to an existing VG
• When a VG runs low on space:
sudo pvcreate /dev/vdc sudo vgextend datavg /dev/vdc sudo vgs # confirm new free space

---
LVM snapshot (basics)
# Create a read-only snapshot of datalv (2G COW space) sudo lvcreate -L 2G -s -n datalv-snap /dev/datavg/datalv # Mount the snapshot read-only sudo mount -o ro /dev/datavg/datalv-snap /mnt/snap # Remove when done sudo umount /mnt/snap sudo lvremove /dev/datavg/datalv-snap

---
LVM status commands
sudo pvs # physical volumes (brief) sudo pvdisplay # physical volumes (detailed) sudo vgs # volume groups (brief) sudo vgdisplay # volume groups (detailed) sudo lvs # logical volumes (brief) sudo lvdisplay # logical volumes (detailed)

---
Summary — LVM — Create, Extend, Reduce Safely
✓ LVM concepts: Term: Description
✓ Create an LVM setup from scratch: Assumes a raw extra disk /dev/vdb (adjust to your device).
✓ Extend an LV (online, no downtime): Or extend and grow in one command:
✓ Reduce an LV (ext4 only — not XFS): ⚠️ XFS cannot be shrunk
✓ Add a new PV to an existing VG: When a VG runs low on space:
✓ LVM snapshot (basics)
✓ LVM status commands